## Slide 1
1

## Slide 2
Ports, Protocols & Services

## Slide 3: 2. Ports, Protocols & Services
3.1 Given a scenario, implement secure protocols
2.1 Explain the importance of security concepts in an enterprise environment

## Slide 4: 2. Ports, Protocols & Services
Communication Protocols
Network Protocols
Domain Name System (DNS)
SPF, DKIM & DMARC
Secure Shell (SSH)
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
Web Browsing Protocols
File Transfer Protocols
Email Protocols
Directory Service Protocols
Voice & Video Protocols
Remote Desktop Protocol (RDP)
Simple Network Management Protocol
Network Timing Protocols

## Slide 5: 3.1 Given a scenario, implement secure protocols
Communication Protocols
  Port
    Ports take you to the correct service.
      “WHERE to communicate”
  Service Protocol
    Establish the rules for systems communicating over the network
      “HOW to communicate”
Example: | 
Protocol | Port
FTP data port (active mode) | tcp/20
FTP control port | tcp/21
SSH | tcp/22
SCP (uses SSH) | tcp/22
SFTP (using SSH) | tcp/22
Telnet | tcp/23
SMTP | tcp/25

## Slide 6: 3.1 Given a scenario, implement secure protocols
Network Protocols
  Transmission Control Protocol (TCP)
    Connection-oriented network communication
    Guaranteed delivery in the right order
    Three-way handshake
  User Datagram Protocol (UDP)
    Connectionless network communication
    Faster, but at the risk of lost packets
    Common with streaming, gaming, VOIP
SYN
SYN / ACK
ACK
UDP
UDP
UDP

## Slide 7
Network Protocols
  Dynamic Host Configuration Protocol (DHCP)
    udp/67 - udp/68
      Automatic IP address allocation
      This is a server with a database of IP addresses that can allocate to requesting hosts
      Attacker could flood a network with IP address requests
      DHCP server can eventually run out of addresses leading to resource exhaustion
  DHCP Snooping
    Security feature that acts like a firewall between untrusted hosts and trusted DHCP servers
    The DHCP snooping feature performs the following activities:
      Validates DHCP messages received from untrusted sources
      Filters out invalid messages

## Slide 8: 3.1 Given a scenario, implement secure protocols
Network Protocols
  Telnet
    tcp/23
      Telecommunication Network
      Login to devices remotely
      Console access
      In-the-clear communication unencrypted
Max 15 00:15:23.431 CRT: #SEC_LOGIN-5-LOGIN_SUCCESS: Login Success [user: msmith] [Source: 10.0.12.45] [localport: 23] at 00:15:23:431 CET Sun Mar 15 2015
Disable telnet and enable SSH to protect data security

## Slide 9: 3.1 Given a scenario, implement secure protocols
Network Protocols
  NETBIOS
    udp/137
    Microsoft legacy naming convention that has a flat namespace of a maximum of 15 characters with a service identifier
      NETBIOS to IP address resolution
      The nbtstat command (NETBIOS STATISTICS) allows you to view statistics for NETBIOS
      PC1 <00>: The <00> represents the workstation service
      PC2 <03>: The <03> represents the messenger service
      PC3 <20>: The <20> represents the server service
PC1 PC2 PC3 | <00> <03> <20> | UNIQUE GROUP UNIQUE | Registered Registered Registered

## Slide 10
Domain Name System (DNS)
  Domain Names & Delegation
.com
.net
.org
.edu
.mil
.gov
company
comcast
comptia
auburn
usaf
dhs
west
east
north
south
company.com.
south.company.com.
user2
user1
user2.west.company.com.
Root Domain
root (.)
Root Domain
Top-Level Domain
Domain
Subdomain/
Web Server Hostname

## Slide 11: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Domain Name Resolution
    DNS Queries
      udp/53
      DNS resolves host names to IP addresses
      Reverse lookup IP address to domain name
    Zone transfers
      tcp/53
      Process of copying the contents of the zone file on a primary DNS server to a secondary DNS server
    Domain Name System Security Extensions (DNSSEC)
      tcp/53
      Secures DNS Traffic

## Slide 12: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  nslookup & dig
    Diagnostic tool for verifying the IP address of a hostname in the DNS server database (DNS Queries)
      nslookup (windows)
      dig (Linux)
    Example: DNS queries
      nslookup google.com
      dig google.com
    Example: Reverse DNS queries
      nslookup 142.251.35.206
      dig - x 142.251.35.206

## Slide 13: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Host DNS Cache
    Stores recently resolved names
  Hosts File
    The hosts file is the mapping of IP Address to Domain Name
  DNS Server (Internal DNS Server)
    Maintains only the hostnames for your domain
Host client checks DNS Cache
Host client checks Host File
Host client checks Local DNS Server

## Slide 14: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Authoritative Response
    Fully-Qualified Domain Name (FQDN) for target host
    Hostname = workstation01
    Domain = company.com
      Fully-Qualified Domain Name (FQDN) = workstation01.company.com.
      IP Address = 192.168.1.26
C:\Users\Administrator>nslookup workstation01 Server: dns.company.com. Address: 192.168.1.254 authoritative answer: Name: workstation01.company.com. Addresses: 192.168.1.26
Notes: https://www.godaddy.com/garage/whats-a-fully-qualified-domain-name-fqdn-and-whats-it-good-for/

## Slide 15: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  nslookup zone transfer
    tcp/53
      Specifies which type of records to search for ( A, PTR, SRV, MX or Any)
        > set type=ANY (All available records)
      Dumps all available records, assuming zone transfers are enabled
      Requested ANY records for the domain mysite.org be dumped in domain "example.org".
        nslookup mysite.org set type=ANY ls-d example.org
nslookup mysite.org set type= ANY ls-d example.org

## Slide 16: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  dig zone transfer
    tcp/53
      AXFR - DNS protocol used during a zone transfer
        example.org - Primary name server
        mysite.org is the domain that we want to initiate a zone transfer for
        mysite.org request or acquires all records from example.org
dig -axfr mysite.org@example.org

## Slide 17: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Mail Server Records (MX)
    The set type=MX command brings back the DNS details on all mail servers in the domain
    The lower preference number is the higher priority (primary mail server)
    The server with the higher preference number is lower priority (backup mail server)
      Back up mail servers may be more vulnerable to attack
      Spammers may deliberately direct mail to one of the backup (high distance) MX servers of a domain first, on the assumption that such a server will have less effective anti-spam filters
Domain | Type | Priority | Host
mysite.org mysite.org | MX MX | 10 20 | mail exchanger = 192.68.102.33 mail exchanger = exchg1.mysite.org
exchg1.mysite.org Internet address = 192.168.102.67 |  |  | 

## Slide 18: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Domain Name System Security Extensions (DNSSEC) (tcp/53)
    Secures DNS Traffic
    Transport Layered Security (TLS) best supports the deployment of DNSSEC
    Evaluates MX record lookup
    Can perform authenticated requests for A and AAA records
    Resource Record Signature (RRSIG)
        Adds a digital signature to each record Resource
        Contains the DNSSEC signature for a record set.
        DNS resolvers verify the signature with a public key, stored in a DNSKEY record.
    DNSKEY record holds a public key used in the DNS authentication process
      Adds public keys to DNS records in the domain
      Contains the public key that a DNS resolver uses to verify DNSSEC signatures in RRSIG records.
    DNSSEC Prevents DNS poisoning

## Slide 19: 3.1 Given a scenario, implement secure protocols
Domain Name System (DNS)
  Exact mail exchange records
    Provides early warning signs from incoming phishing attacks.
    Drastically reduce your company’s risk of phishing.
    You can take immediate steps to block inbound emails from malicious domains.

## Slide 20: 3.1 Given a scenario, implement secure protocols
SPF, DKIM & DMARC
  These are mainly authorization, authentication protocols and mechanisms relying mainly on DNS to protect your mail from phishing and spoofing.
    Domain Keys Identified Message (DKIM)
    Sender Policy Framework (SPF)
    Domain-based Message Authentication, Reporting, and Conformance (DMARC)

## Slide 21: 3.1 Given a scenario, implement secure protocols
SPF, DKIM & DMARC

## Slide 22: 3.1 Given a scenario, implement secure protocols
SPF, DKIM & DMARC
  Sender Policy Framework (SPF)
    Receiving mail servers verify that incoming messages come from your domain.
      SPF specifies the mail servers that are allowed to send email for your domain.
      Protects your domain against spoofing.
      Prevents your outgoing messages from being marked as spam.
  Domain Keys Identified Mail (DKIM)
    Signature-based Email Authentication technique.
      Standard to help prevent spoofing on outgoing messages sent from your domain
      Ensures integrity of sensitive information that is exchanged through email.
      Adds an encrypted signature to the header of all outgoing messages.
      Email servers that get signed messages use DKIM to decrypt the message header.
      Verifies the message was not changed after it was sent.
DKIM

## Slide 23: 3.1 Given a scenario, implement secure protocols
SPF, DKIM & DMARC
  Domain-based Message Authentication, Reporting, and Conformance (DMARC)
    Detects when messages don't actually originate from the Internet domain they claim to have been sent from.
    Sender messages are protected by SPF and/or DKIM
    Tells a receiver what to do if neither of those authentication methods passes
    Checks the “From” address domain and compares it with the “Mail from” domain
    Protects a domain from being used in outgoing business email compromise attacks
      Phishing emails
      Spam email
      Other cyber threat activities
DMARC

## Slide 24: 3.1 Given a scenario, implement secure protocols
Secure Shell (SSH)
  tcp/22
    Encrypted console communication
      Remote access
      Encrypted remote console login
      Encrypts data
      Command-line Interface (CLI)
      Replaces Telnet
    File Transfer
      Secure File (SFTP)
      Secure File Copy (SCP)
      Upload files onto a remote server using a scheduled task
    Routing and switching
      Encrypted terminal communication
      Secure network device configuration
    Authentication methods
      Public keys are generated for certificate-based authentication (SSH Keys)
      Username and password
      Microsoft environment, use Kerberos to produce a ticket

## Slide 25: 3.1 Given a scenario, implement secure protocols
Secure Shell (SSH)
  ssh key-based authentication
    generate a RSA public and private key pair on the administrator's desktop
      ssh-keygen – t rsa
    Copy the public key to the SSH server
      ssh-copy-id
    Test ssh keys
      ssh root@server
Remote User
Private SSH Key
Remote Directory
public SSH key
tcp/22 Control & Data

## Slide 26: 3.1 Given a scenario, implement secure protocols
Secure Shell (SSH)
  Secure Copy (SCP)
    tcp/22
      Is a command-line utility that allows you to securely copy files and directories between two locations.
      With scp you can copy a file or directory:
        From your local system to a remote system.
        From a remote system to your local system.
        Between two remote systems from your local system.
scp file.txt remote_username@10.10.0.2:/remote/directory
Name of the file we want to copy
User on the remote server
Server IP address
Path to the directory you want to copy the file to
Copy a Local File to a Remote System

## Slide 27: Given a scenario, implement secure protocols
File Transfer Protocols
  Secure File Transfer Protocol (SFTP)
    System generates a public-private key pair
    You link your public key to your account on the SFTP server
    Client will produce a signature with private key that the server can confirm with the already-stored public key
    public and private keys match up, the connection is established
SFTP Client
Private SSH Key
SFTP Server
public SSH key
Keys - Commands - Data
Encrypted Tunnel

## Slide 28: 3.1 Given a scenario, implement secure protocols
Secure Shell (SSH)
  Secure File Transfer Protocol (SFTP)
    Downloading Files:
      sftp> get filename.zip
    Uploading Files:
      sftp> put filename.zip
    Create a new directory on the remote server:
      sftp> mkdir directory_name
    Change the permissions of a file on the remote system:
      sftp> chmod 644 file_name
    Change the owner of a file on the remote system:
      sftp> chown user_id file_name
sftp remote_username@10.10.0.2
User on the remote server
Server IP address or hostname
Establishing an SFTP connection

## Slide 29: 3.1 Given a scenario, implement secure protocols
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
  HTTPS tcp/443
    Used to encrypt communications on the Internet
    Used to secure network communication
    Provides data integrity and communication privacy
    Used by web browsers to protect connections between web applications and web servers.
    TLS protects data in transit and is an upgraded version of SSL
    Manage the SSL/TLS certificates on your local computer using a Graphical User Interface (GUI)

## Slide 30: 3.1 Given a scenario, implement secure protocols
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
  Many other TCP-based protocols use TLS/SSL
    Typically, when a service uses a secure connection the letter S is appended to the protocol name, for example, HTTPS, SMTPS, FTPS, SIPS.

## Slide 31: 3.1 Given a scenario, implement secure protocols
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
  Cipher Suites
    TLS 1.2
      Elliptic Curve Diffie-Hellman Ephemeral mode (ECDHE) for session key Agreement (key exchange)
      RSA signatures/Public Key
      128-bit AES-GCM (Galois Counter Mode) for bulk encryption (ESP)
      256-bit SHA for HMAC functions (AH)
TLS_ECDHE_RSA_WITH_AES128_GCM_SHA256

## Slide 32: 2.8 Summarize the basics of cryptographic concepts
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
  TLS 1.3
    Uses simplified and shortened cipher suite
    Typical TLS 1.3 cipher suite appears as follows:
      Only ephemeral key agreement supported in 1.3
      Signature type supplied in the certificate
      Cipher suite only lists bulk encryption key strength and mode of operation (AES_256_GCM)
      Cryptographic hash algorithm (SHA384) used with each new hash key derivation function (HKDF)
      Shared secret established by D-H key agreement used to derive symmetric session key
TLS_AES_256_GCM_SHA384

## Slide 33: 3.1 Given a scenario, implement secure protocols
Secure Socket Layer (SSL) /Transport Layer Security (TLS)
  SSL/TLS Handshake
TLS/SSL certificate & public key sent back
Client request SSL/TLS Session
Session Key encrypted with web server public key (RSA)
Encrypted session key sent to server: Client creates session key
Pre-master key decrypted using private key
This is the server Public key decrypted with the servers Private key
Session key is also decrypted
Session encrypted with symmetric session key
TLS_ECDHE_RSA_WITH_AES128_GCM_SHA256
ECDHE - Key Exchange
RSA - Web Server Public Key
AES128_GCM - Session Key

## Slide 34: 3.1 Given a scenario, implement secure protocols
Web Browsing Protocols
  Hypertext Transport Protocol (HTTP)
    tcp/80
    Unsecure
    Enables clients (typically web browsers to request recourses from an HTTP from an HTTP server.
      GET: Something is retrieved FROM a server.
      POST: Something is sent TO a server..
Web Logs |  |  |  |  |  | X
Time | SRC IP | SRC Port | Destination IP | DST Port | Request Code | URL
12:01:02 | 192.168.1.6 | 9087 | 85.10.211.94 | 80 | GET | company.com
12:01:03 | 192.168.1.7 | 3456 | 85.10.211.94 | 80 | POST | company.com
12:01:04 | 192.168.1.8 | 12536 | 85.10.211.94 | 80 | POST | company.com

## Slide 35: 3.1 Given a scenario, implement secure protocols
Web Browsing Protocols
  Hypertext Transport Protocol Secure (HTTPS)
    tcp/443
    Encrypts web traffic with SSL or TLS
    Indication of a secure HTTPS session lock icon including HTTPS in the URL field
    Transfer files through the Internet in a secure manner
    Uses x.509 certificates for authentication
Example:
A web server should also utilize the latest security techniques and standards Install an X- 509-compliant certificate Enable and configure TLS on the server
+
=

## Slide 36: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  Trivial File Transfer Protocol (TFTP)
    udp/69
      Unsecure
      File transfer using UDP
      Is used to transfer smaller amounts of data
      Communication with network devices
      Not an essential protocol on most networks (commonly disabled)

## Slide 37: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  File Transfer Protocol (FTP)
    tcp/20 - tcp/21
      Sends and receives files between systems
      Unencrypted file transfer
    FTP is a client-server protocol that relies on two communications channels between the client and server:
    Command channel for controlling the conversation tcp/21
    Data channel for transmitting file content tcp/20
    FTP sessions work in active or passive modes
Command Channel (control)
Data Channel
Port 21
Port 20
or
High Port
(1024+)
FTP Client
FTP Server

## Slide 38: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  File Transfer Protocol (FTP)
    Active mode
      Client initiates a session via a command channel request
      Server creates a data connection back to the client and begins transferring data
FTP Client
FTP Server
FTP control connection to port 21 from high port
Port 20
High Port
(1024+)
Active FTP
FTP data connection initiation from port 20 on server to high port on client

## Slide 39: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  File Transfer Protocol (FTP)
    Passive mode.
      The server uses the command channel to send the client the information it needs to open a data channel.
      Passive mode has the client initiating all connections, it works well across firewalls and network address translation gateways.
FTP Client
FTP Server
FTP control connection to port 21 from high port
FTP data connection initiation from high port on client to high port on the server
High Port
(1024+)
Passive FTP (PASV)
High Port
(1024+)

## Slide 40: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  FTP Secure (FTPS)
    tcp/990 for the FTPS control channel
    tcp/989 for the FTPS data channel
      Authentication performed via x.509 certificates
      Requires a server X.509 certificate and private key
      Negotiates a secure session using TCP port 990 for the control channel and 989 for the data channel
    This approach enables implicit Transport Layer Security (TLS) as soon as an FTP connection is established.
Public Key
(Public x.509 Certificate)
Private key
(Private x.509 Certificate)
FTP Client
FTP Server
Port 990 Control Channel
Port 989 Data Channel
Encrypted SSL/TLS Tunnel

## Slide 41: 3.1 Given a scenario, implement secure protocols
File Transfer Protocols
  FTP over explicit SSL/TLS (FTPES).
    This approach enables explicit TLS support by upgrading an FTP connection over port 21 to an encrypted connection.
    Commonly used approach by web and file sharing services to enable secure file transfers.
    Client must request security; if they do not, the session will be refused.

## Slide 42: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Email Architecture
    SMTP – Outgoing or Send Mail
    POP3 / IMAP4 – Incoming or Receive Mail
IMAP4/POP3
SMTP
Internet
SMTP Server
Mail Transfer Agent
(MTA)
Mail Sender
SMTP
SMTP Server
Mail Exchange
(MX)
Mail Sender

## Slide 43: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Simple Mail Transfer Protocol (SMTP)
    Outgoing mail
      Transfers email from client -> server
      Also transfers from server -> server
tcp/25 - Unsecure

## Slide 44: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Simple Mail Transfer Protocol Secure (SMTPS)
    Prevents emails in plain text from being sniffed
  tcp/465 – SSL
  tcp/587 – TLS
+
=

## Slide 45: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Post Office Protocol v3 (POP3)
    Incoming mail
      Transfers emails from server -> client
      Deletes copy of e-mail after transfer and does not save to the server
tcp/110 - Unsecure

## Slide 46: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Post Office Protocol v3 Secure (POP3)
    Provides encrypted logins to the email server
tcp/995 - Secure
+
=
tcp/995 - Secure

## Slide 47: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Internet Message Access Protocol v4 (IMAP4)
    Incoming mail
      Transfers emails from server -> client
      Receives and stores email and remains on the server, example Gmail
tcp/143 - Unsecure

## Slide 48: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Internet Message Access Protocol Secure (IMAPS)
    Provides encrypted logins to the email server
+
=
Secure – SSL/TLS
tcp/993

## Slide 49: 3.1 Given a scenario, implement secure protocols
Email Protocols
  Secure/Multipurpose Internet Mail Extensions (S/MIME)
Example:
A security consultant is setting up a new electronic messaging platform and wants to ensure the platform supports message integrity validation. The consultant should recommend S/MIME protocol (digital signature)
    Used for digital signature between two people
    Encrypt and sign email using S/MIME
    Supports employs certificates generated by the PKI
    Implements a stream cipher

## Slide 50: 3.1 Given a scenario, implement secure protocols
Directory Service Protocols
  Lightweight Directory Access Protocol(LDAP)
    Port tcp/389
    LDAP is an open application protocol and works outside of the Windows structure, focusing on Unix and Linux environments.
    Stores objects such as users and computers as x.500 objects
    Used to communicate with directories over network
    The protocol searches and compares the credentials to what the LDAP server has stored for the authenticating user
      If the username and password match what’s listed in the directory, LDAP authenticates the user.

## Slide 51: 3.1 Given a scenario, implement secure protocols
Directory Service Protocols
  LDAP Secure (LDAPS)
    tcp/636
    LDAPS allows for the encryption of LDAP data (which includes user credentials) in transit protecting against credential theft.
      LDAP traffic is encrypted
      Cannot be monitored or sniffed
      SSL or TLS use with LDAPS
      Using X.509-compliant certificate that is signed by a trusted CA
+
=

## Slide 52: 3.1 Given a scenario, implement secure protocols
Directory Service Protocols
  Active Directory
    Microsoft’s proprietary solution for accessing and managing directories
    Windows Active Directory supports both LDAP and Kerberos for authentication
    LDAP and Kerberos can be used together one at a time or simultaneously as well.
    By default, Windows uses Kerberos for authentication purposes
      LDAP used for the same and is used for organizing objects within the Active Directory domain such as:
        User accounts
        Computers
        Organization units (OUs)

## Slide 53: 3.1 Given a scenario, implement secure protocols
Voice & Video Protocols
  Session Initiated Protocol Secure (SIPS)
    udp/5061
      Initiates and establishes the session
      Encrypts credentials used for session authentication on connections to the Private Branch Exchange (PBX)
      Allows communication over the Internet, and VoIP communication using
        Computers
        Tablets
        Smartphones
+
=

## Slide 54: 3.1 Given a scenario, implement secure protocols
Voice & Video Protocols
  Secure Real-time Transport Protocol (SRTP)
    udp/5061
    RTP transfers voice and video traffic
    Voice traffic should be placed in its own VLAN to ensure reliability
    Protocol enables secure, real-time delivery of audio and video over an IP network
    SRTP provides the following for RTP:
      Confidentiality – AES Encryption
      Integrity – Message authentication

## Slide 55: 3.1 Given a scenario, implement secure protocols
Voice & Video Protocols
  Secure Real-time Transport Protocol (SRTP)
  Session Initiated Protocol Secure (SIPS)
Certificate
Certificate
SIP over TLS
SIP over TLS
SIP over TLS
Private Branch Exchange
(PBX)
Private Branch Exchange
(PBX)
“SIPS initiates the call”, encrypts credentials
Data / Voice transported with UDP, encrypted by SRTP
SIPS

## Slide 56: 3.1 Given a scenario, implement secure protocols
  Remote Desktop sessions operate over an encrypted channel, preventing anyone from viewing your session by listening on the network.
    A vulnerability in the method used to encrypt sessions in earlier versions of RDP
    Vulnerability can allow unauthorized access to your session using a man-in-the-middle attack
Remote Desktop can be secured using SSL/TLS
Remote Desktop Protocol (RDP)
  tcp/3389 – udp/3389
    Graphical display of remote devices (GUI)
    Connect to remote systems
    Remote Desktop Connection
    Windows Remote Assistance

## Slide 57: 3.1 Given a scenario, implement secure protocols
Remote Desktop Protocol (RDP)
  Remote Desktop Gateway (RDG or RD Gateway)
    provides a secure encrypted connection to the session remote desktop session host via RDP.
      It enhances control by removing all remote user access to your system and replaces it with a point-to-point remote desktop connection.
      Access the server/session host using RDP on a port other than the typical registered port for the RDP protocol
RDP Client
SSL Tunnel tcp/443
SSL Tunnel tcp/443
Tcp/3389
Firewall
Remote Desktop
Gateway
Remote Desktop
Session Host

## Slide 58: Given a scenario, implement secure protocols
Remote Access Protocols
  Administrators connect to servers remotely using protocols such as:
    Secure Shell (SSH)
    Remote Desktop Protocol (RDP)
    Virtual Private Networks (VPN)
    Telnet Port 23 Run remote command—unsecure (cleartext)
  Netcat (nc) is useful for remotely administering servers
    Netcat is to establish connections (sockets)
    Linux administrators use Netcat when connecting to remote systems
    Secure the Netcat transmissions with SSH

## Slide 59: 3.1 Given a scenario, implement secure protocols
Simple Network Management Protocol
  Simple Network Management Protocol
    udp/161 for SNMP Managers communicating with SNMP Agents
      Networking protocol used for the management and monitoring of network-connected devices in Internet Protocol networks
      Accessible using their IP address
      SNMP protocol is embedded in multiple local devices such as:
        Routers
        Switches
        Servers
        Firewalls
        Wireless access points
    udp/162 Simple Network Management Protocol Trap (SNMPTRAP)
      when agents send unsolicited Traps to the SNMP Manager

## Slide 60: 3.1 Given a scenario, implement secure protocols
Simple Network Management Protocol
  Simple Network Management Protocol 3 (SNMPv3)
    Version 3 added encrypted communication instead of SNMPv1 and v2
    Encrypts credentials and traffic between network devices
    Includes authentication and encryption of SNMP messages as well as protecting packets during transit.
      The first version of SNMP and SNMPv2 had vulnerabilities, such as passing passwords or traffic across the network is in clear-text
+
=

## Slide 61: 3.1 Given a scenario, implement secure protocols
Time Synchronization Protocols
  Network Time Protocol (NTP)
    udp/123
    Most commonly used protocol for time synchronization
  Simple NTP (SNTP)
    udp/123
    Not as accurate as the result from NTP
    Typically for smaller systems with less dedicated processing power

## Slide 62: 3.1 Given a scenario, implement secure protocols
Time Synchronization Protocols
  Public NTP Servers vs. Local NTP Servers
    There are two types of NTP servers that you can use to provide UTC time to your network:
      External (public servers)
        A external time server is owned and operated by a third party
        Made available for use over the Internet
        Requires an open port on the firewall making your network vulnerable
      Internal (local servers)
        NTP servers are those you own yourself and install in your premises
        Physical network connection between your servers and clients
        Internal time servers are the safer, more reliable option

## Slide 63: 3.1 Given a scenario, implement secure protocols
Time Synchronization Protocols
  External (Public) NTP Servers vs. Internal (Local) NTP Servers
External NTP Servers
Requires an open port on the firewall making your network vulnerable
Internal NTP Servers
NTP Server is behind the firewall leaving your network fully protected

## Slide 64: 3.1 Given a scenario, implement secure protocols
Time Synchronization Protocols
  Stratum 0: The atomic time clock or reference time server
  Stratum 1: An internal time server that synchronizes its time with a Stratum 0
  Stratum 2: An internal time server on a remote subnet that synchronizes its time with the Stratum 1 time server
    A Stratum 0 time server is the ultimate authority in a Stratum time server environment
      It is the atomic clock or GPS that time should be synchronized with
      If there is no internal Stratum 1 NTP server, then we will use an internal Stratum 0 NTP server
Example:
Due to regulatory requirements, server in a global organization must use time synchronization. The following represents the MOST secure method of time synchronization The server should connect to internal Stratum 0 NTP servers for synchronization

## Slide 65: 3.1 Given a scenario, implement secure protocols
Time Synchronization Protocols
NTP Time Server
GPS
Antenna
Server/Workstations
Switch/Router
Ethernet
Clock
  Stratum 0
    Atomic clock
    GPS clock
    Very accurate
  Stratum 1
    Synchronized to stratum 0 servers
    Primary time servers
  Stratum 2
    Sync’d to stratum 1 servers
GPS Satellite

## Slide 66: Answer the questions
During a security audit of a company’s network, unsecure protocols were found to be in use. A network administrator wants to ensure browser-based access to company switches is using the most secure protocol. Which of the following protocols should be implemented?
  SSH2
  TLS1.2
  SSL1.3
  SNMPv3
Confidential emails from an organization were posted to a website without the organization’s knowledge. Upon investigation, it was determined that the emails were obtained from an internal actor who sniffed the emails in plain text. Which of the following protocols, if properly implemented, would have MOST likely prevented the emails from being sniffed? (Select two.)
  SMTPS
  S/MIME
  POP3
  IMAP4
  SMTP
Notes: Answers:
1. d (SNMPv3 supports the strongest cipher suite available TLSv1.3 and TLSv1.2 and SSH is CLI not browser-based)
2. a and b

## Slide 67: QUESTIONS

## Slide 68: 2. Ports, Protocols & Services
3.1 Given a scenario, implement secure protocols
2.1 Explain the importance of security concepts in an enterprise environment

## Slide 69
69