## Slide 2
Securing Wireless & Mobile Solutions

## Slide 3: Securing Wireless & Mobile Solutions
3.4 Given a scenario, install and configure wireless security settings
3.5 Given a scenario, implement secure mobile solutions

## Slide 4: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
Authentication Protocols
Installation Considerations
Controller and Access Point Security

## Slide 5: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Open mode
    No Credentials
    No authentication
    No security
  Equivalent Privacy (WEP)
    WEP RC4
    Weakest form of wireless security, with a 40-bit key
    Easy to crack within seconds by an Initialization Vector (IV) attack

## Slide 6: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Wi-Fi Protected Access (WPA)
    WPA uses RC4-128 in TKIP
    WPA replaced WEP as it uses the Temporal Key Integrity Protocol (TKIP)
    Uses RC4 128 bit stream cipher
    TKIP is vulnerable to replay attacks
  WPS (Wi-Fi Protected Setup)
    Non-credentialed Authentication
    Password is already stored
    Press push button to get connected to the wireless network
    Commonly used to connect IoT

## Slide 7: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Wi-Fi Protected Access Version 2 (WPA2)
    Much stronger than WPA
    Uses Counter Mode with the Cipher Block Chaining Message Authentication Code Protocol (CCMP) also known as:
      AES128_CCM
    Features of WPA2 include:
      WPA2-TKIP
      WPA2-CCMP
      WPA2-CCMP + TKIP
      WPA2- PSK (Pre-Shared Key)
      WPA2-Enterprise
      WPA2-WPS

## Slide 8: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Pre-Shared Key (PSK)
    User enters the password for home network access
    Home version for WPA2 known as Personal Mode
  WPA2-CCMP
    Strongest version of WPA2
  WPA2-TKIP
    Provides compatibility with legacy systems
  WPA2-CCMP + TKIP
    Provides strong security for AES compatible systems
    Provides compatibility with legacy systems
WPA2 Personal
PSK-mode
TKIP and/or CCMP
AES-128 (for CCMP)
RC4-128 (for TKIP)
Security Mode
Authentication
Encryption
Cipher/Algorithm

## Slide 9: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  WPA2-Enterprise
    Corporate version of WPA2
    Centralized domain environment
    AAA server combines with 802.1x
    Uses server certificates for authentication
      RADIUS - user management
      TACACS+ - device management
    802.1x uses EAP variant
      PEAP
      EAP-FAST
      EAP-TLS
      EAP-TTLS
WPA2 Enterprise
Enterprise-mode
802.1x using EAP
CCMP
AES-128 (for CCMP)
Security Mode
Authentication
Encryption
Cipher/Algorithm

## Slide 10: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Wi-Fi Protected Access Version 3 (WPA 3)
    Released in 2018 to address the weaknesses in WPA2
    Uses a much stronger 256-bit Galois/Counter Mode Protocol (GCMP-256) for encryption also known as:
      AES256_GCM
    Features of WPA3 include:
      WPA3-SAE (Simultaneous Authentication of Equals)
      PMF (Protected Management Frames)
      Wi-Fi Easy Connect
      Wi-Fi Enhanced Open
      WPA3-SAE Transition
      WPA3-Enterprise

## Slide 11: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Protected Management Frames (PMF)
    WPA3 uses Protected Management Frames (PMF)
      PMF Prevents attackers from capturing the encryption keys (IV Attack)
  Wi-Fi Easy Connect:
    Easy to connect IoT devices, such as a smartphone, by simply using a QR code
  Wi-Fi Enhanced Open (OWE)
    Enhancement of WPA2 open authentication
    Uses encryption for open authentication
    No password is required
    Prevents eavesdropping as it uses PMF
Notes: See the Student Resource Book for pictures of what the configurations look like.

## Slide 12: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Personal Mode
    WPA3-SAE
      Home version of WPA3 known as WPA3-Personal
      Replaces the WPA2-PSK
      Protects against brute-force attacks
      Provides Perfect Forward Secrecy (PFS)
      Ensures session keys cannot be compromised
      Simpler passwords for home network access
      Immune to offline attacks
    WPA3-SAE Transition
      Allows backwards compatibility with WPA2-PSK
WPA3-Personal
SAE-mode
Transition-mode
CCMP
AES-128 (for CCMP)
Security Mode
Authentication
Encryption
Cipher/Algorithm

## Slide 13: 3.4 Given a scenario, install and configure wireless security settings
Layer 2 Security
WPA2+WPA3
Personal
WPA2
WPA3
CCMP128
Encryption Cipher
Policy
FAST Transition
FAST Transition
Disabled
Required
1
200
PMF
Comeback timer(1-
10sec)
SA Query Timeout(100-
500msec)
Protected Frame Management
ASCII
PSK Format
P@$$w0rd12345
SAE
Enable
Authentication Key Management
WPA2+WPA3 PARAMETERS
Security Type
MAC Filtering
Layer 2 Security: WPA2+WPA3
Security Type: Personal mode
Policy WPA3 + WPA2 Disabled = WPA3 SAE mode
Encryption Cipher: CCMP128(AES)
  Also known as AES-128 in CCM
PMF is Required
SAE is enabled by default
Authentication Methods
WPA3 SAE mode
Notes: I hide these four slides because these images are in the CompTIA Student book and they can see them there.

## Slide 14: 3.4 Given a scenario, install and configure wireless security settings
Layer 2 Security
WPA2+WPA3
Personal
WPA2
WPA3
CCMP128
Encryption Cipher
Policy
FAST Transition
FAST Transition
Disabled
Optional
1
200
PMF
Comeback timer(1-
10sec)
SA Query Timeout(100-
500msec)
Protected Frame Management
ASCII
PSK Format
P@$$w0rd12345
PSK
PSK-SHA2
SAE
Enable
Enable
Enable
Authentication Key Management
WPA2+WPA3 PARAMETERS
Security Type
MAC Filtering
Layer 2 Security: WPA2+WPA3
Security Type: Personal mode
Policy WPA3 + WPA2 Enabled = WPA3 Transition mode
Encryption Cipher: CCMP128(AES)
  Also known as AES-128 in CCM
PMF is configured as Optional; if configured as Required
WPA2 devices would not be able to connect
All AKM’s can be configured based on PMF selection
SAE is enabled by default
Authentication Methods
WPA3 Transition mode

## Slide 15: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Enterprise Mode
    Corporate version security mode
    Centralized domain environment
    AAA server combines with 802.1x
    Uses AAA server certificates for authentication
      RADIUS AAA Server - user management
      TACACS+ AAA Server - device management
    802.1x uses EAP variant
      PEAP
      EAP-FAST
      EAP-TLS
      EAP-TTLS
Enterprise Mode
Enterprise-mode
802.1x using EAP
CCMP (for WPA2)
GCMP (for WPA3)
AES-128 (for CCMP)
AES-256 (for GCMP)
Security Mode
Authentication
Encryption
Cipher/Algorithm

## Slide 16: 3.4 Given a scenario, install and configure wireless security settings
Layer 2 Security
WPA2+WPA3
Enterprise
Encryption Cipher
Policy
FAST Transition
FAST Transition
Disabled
Not Required
1
200
PMF
Comeback timer(1-
10sec)
SA Query Timeout(100-
500msec)
Protected Frame Management
SUITEB192-1X
Enable
Authentication Key Management
WPA2+WPA3 PARAMETERS
Security Type
MAC Filtering
Layer 2 Security: WPA2+WPA3
Security Type: Enterprise mode
Policy WPA3 + WPA2 Enabled
WPA2 Enterprise mode
Encryption Cipher: CCMP256
SUITEB128-bit Mode not offered by WPA2-Enterprise.
PMF is Required
Authentication Methods
WPA2 Enterprise mode
WPA2
WPA3
CCMP128
CCMP256
GCMP128
GCMP256

## Slide 17: 3.4 Given a scenario, install and configure wireless security settings
Layer 2 Security
WPA2+WPA3
Enterprise
WPA2
WPA3
CCMP128
Encryption Cipher
Policy
FAST Transition
FAST Transition
Disabled
Required
1
200
PMF
Comeback timer(1-
10sec)
SA Query Timeout(100-
500msec)
Protected Frame Management
SUITEB192-1X
Enable
Authentication Key Management
WPA2+WPA3 PARAMETERS
Security Type
MAC Filtering
CCMP256
GCMP128
GCMP256
Layer 2 Security: WPA2+WPA3
Security Type: Enterprise mode
Policy WPA3 + WPA2 Enabled
WPA3 Enterprise mode
Encryption Cipher: GCMP256
SUITEB192-bit Mode offered by WPA3-Enterprise.
When used PMF shall be set to required
SUITEB192-bitlevel security.
TLS_ECDHE_RSA_WITH_AES_256_GCM_SHA384
TLS_ECDHE_ECDSA_WITH_AES_256_GCM_SHA384
PMF is Required
Authentication Methods
WPA3 Enterprise mode

## Slide 18: 3.4 Given a scenario, install and configure wireless security settings
Authentication Methods
  Captive Portal
    Basic accountability for access to the public network
    Allows guests to use an "open" WiFi network
    Background reconnection for mobile users
    Visitors accepts the AUP or terms of service

## Slide 19: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  PPP (Point-to-Point Protocol)
    Used when authentication needs to be sent across these networks.
      PAP (Password Authentication Protocol)
        Passwords are transmitted as clear text and can be easily captured.
        2-way handshake
      CHAP/MSCHAP (Microsoft Challenge Handshake Authentication Protocol)
        Uses a challenge-response mechanism with password encryption
        Client send cryptographic function of the password (password hash)
PAP
CHAP

## Slide 20
Introduction to the Point-to-Point Protocols
Notes: Introduction to the Point-to-Point Protocols
https://www.youtube.com/watch?v=7PtTn38f4os
See also:
The three phases of PPP including PAP and CHAP
https://www.youtube.com/watch?v=hneSiV0N-hM
This is a very good video, and she’s got all her facts right, but she makes one big mistake at the very end. Hashes are compared, they cannot be decrypted. Hashes are one-way functions.
Here is what is on the summary slide in the first video:
PPP operates at layer 2 of the OSI model
Purpose: transport layer 3 protocols over serial links
Made up of LCP and NCP
LCP
  Link establishment
  Authentication
  Error detection
  Multilink
  Load balancing
NCP
  How to transmit the layer 3 protocols

## Slide 21: 802.1x Port Security
21

## Slide 22: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  IEEE 802.1x
    Standard for Port-Based Network Access Control (PNAC)
    Provides protected authentication for secure wired and wireless networks
      Switch (LAN)
      Access Point (Wireless)
      Wireless LAN Controller (WLC)
    Ensures access is granted only after a user or device has been authenticated
      EAPoL (EAP over LAN)
      EAPoW (EAP over Wireless)
    Authentication Server
      RADIUS
      TACACS+

## Slide 23: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  Extensible Authentication Protocol (EAP)
    Authentication framework allowing point-to-point connections
    Commonly used with wireless communication
      EAP TLS
      PEAP (Protected Extensible Authentication Protocol)
      EAP-TTLS
      EAP-FAST (Flexible Authentication via Secure Tunneling)
        Cisco proprietary. Replaced LEAP.
        Server generates a key and provides it to trusted clients
        Does not use certificates but can support the use of them

## Slide 24: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  EAP-TLS (EAP over Transport Layer Security)
    Most secure (compared to other EAP methods)
    No user intervention
    Needs X.509 certificates installed on the endpoints for mutual authentication
      Requires certificate on the clients
      Requires certificate on 802.1x server

## Slide 25: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  PEAP (Protected EAP)
    Encapsulated the EAP data and made it more secure for WLANS
    Accomplishes this by using tunneling between PEAP clients and an authentication server
    Provides mutual authentication
    Requires certificate on 802.1x server
    Supports client usernames and EAP-based password inner authentication methods passwords
      EAP-MSCHAPv2 (PEAPv0)
      EAP-GTC (PEAPv1)
    Client sends encrypted username and password hash to identify itself
            Username password hash protected by encrypted TLS tunnel
                Client Authenticated by the Radius AAA Server

## Slide 26: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  EAP-TTLS (EAP over Transport Layer Security)
    Client authenticates RADIUS AAA Server certificate
    Creates a tunnel for the users' credentials to travel through.
    Secures older authentication methods like Password Authentication Protocol
      EAP-TTLS/PAP
    Client sends Clear text username and password to identify itself
    Username and password protected by encrypted TLS tunnel
    Client Authenticated by the Radius AAA Server

## Slide 27: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  RADIUS (Remote Authentication Dial-In User Service)
    Determines user identity by communicating with the organization’s directory, typically over the LDAP or SAML protocol
      Provide authentication, authorization, and accounting in one service
      UDP 1812 - Authentication and Authorization
      UDP 1813 - Accounting
      Centrally managed authentication
      User Access control
  RADIUS Federation
    Use RADIUS with federation
    Members of one organization can authenticate to the network of another organization
    Use their normal credentials
  Diameter
    AAA Server that is a more modern version of RADIUS that works on TCP

## Slide 28: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  TACACS+ (Terminal Access Controller Access-Control System Plus)
    Provide Separate control of each service: authentication, authorization, and accounting
    TCP 49
    Centrally managed authentication
    Device access management
      Used to control specific commands that can be executed on a network infrastructure device
      Network infrastructure device such as VOIP Services

## Slide 29: 3.4 Given a scenario, install and configure wireless security settings
Authentication Protocols
  IEEE 802.1x
Client/User
Switch/Access Point/WLC
Supplicant
Authenticator
802.1x
EAPoL- EAPoW
RADIUS
RADIUS/TACACS+
EAP Types
EAP Types
Client IP:
Shared Secret:
AAA Server IP:
Shared Secret:
Auth Port:
Acct Port:
EAPoR
ESSID:
Network Auth:
Data Encryption:
ESSID:
Network Auth:
Data Encryption:
Authentication
Server

## Slide 30: 3.4 Given a scenario, install and configure wireless security settings
Installation Considerations
  Site Survey
    Identify what could cause interference with the wireless network
      Determine intermittent connectivity
  WAP Placement
    There are many things that could interfere with or prevent your wireless network from working
      Load-bearing walls
      Cordless phones
      Microwaves
      Elevators
      Metal frames
      Metal doors
      Radio waves

## Slide 31: 3.4 Given a scenario, install and configure wireless security settings
Installation Considerations
  Heat Map
    A heat map shows your wireless coverage
    Red and orange areas indicate good coverage
    Blue areas indicate poor coverage

## Slide 32: 3.4 Given a scenario, install and configure wireless security settings
Installation Considerations
  Recommended channels to use on 2.4Ghz are Channel 1, 6 & 11.
    Channels do not overlap into each other
      Channel 1: Your first wireless device (router)
      Channel 11: Your second wireless device
      Channel 6: Your third wireless device
      5 GHz, it is recommended to use at least 40 MHz channel width
Do you know what a “thin” access point is?
Notes:     Fat AP - Standalone WAP, similar to that used at home
    Thin AP - Used to manage multiple APs remotely

## Slide 33: 3.4 Given a scenario, install and configure wireless security settings
Installation Considerations
  Wireless Standards
    Mixed mode allows backwards compatibility with standards and devices
IEEE Standard | Frequency Band | Maximum Allowable Streams
802.11a | 5 GHz | 1
802.11b | 2.4 GHz | 1
802.11g | 2.4 GHz | 1
802.11n | 2.4 GHz and 5 GHz | 4
802.11ac | 5 GHz | 8
802.11ax | 2.4 GHz and 5 GHz | 16

## Slide 34: 3.4 Given a scenario, install and configure wireless security settings
Controller and Access Point Security
    WiFi Analyzer can be used to detect receive signal strength and uncloak a disabled SSIDs

## Slide 35: 3.4 Given a scenario, install and configure wireless security settings
Controller and Access Point Security
  Default Username and Password
    Change default username and password and configure admin password (master password)
  Disable the Security Set Identifier (SSID)
    Protect the wireless network by disabling the SSID so that it is not broadcast
  MAC Filtering
    Only those devices with a MAC address listed will be allowed access

## Slide 36: 3.5 Given a scenario, implement secure mobile solutions
Connection Methods and Receivers
  Tethering
  NFC/RFID
  Bluetooth / Personal Area Network (PAN)
  SATCOM
  Wi-Fi Direct/Ad Hoc
        Allows two Wi-Fi devices to connect without requiring a WAP
Mobile device management (MDM)
Enforcement and Monitoring
Deployment Models
Do you know what “sideloading” is?
Do you know what Blueborne is?
Notes:   Bluetooth
    Devices have a range of about 10 meters
    The devices are paired using a code to connect
    provide a personal area connection (PAN)
  Secure Satellite Communications (SATCOM)
    Dish at one location that connects point to point with a dish in another location

## Slide 37: 3.5 Given a scenario, implement secure mobile solutions
Mobile Device Management (MDM)
  Management console that allows security administrators to control, secure, and enforce policies on mobile devices
  Mobile Devices
    Smartphones
    Tablets
    Other endpoint devices (UEM)
Download Manager
  Controls the number of connections
  Speed of downloading onto a mobile device
Mobile Application Management (MAM)
  Uses whitelists for authorized applications
  Ability to install mobile tools
Content Management
  Prevents confidential or business data from being shared with external users
  Containerization
  Policies
    Remote wipe capabilities (Containerization)
    Geolocation services
    Patch management and reporting
    Mandatory screen locks
    Ability to require passcodes and pins
    Ability to require encryption
    Mobile device OSs must be patched up to the latest release (Posturing)
    Ability to prevent the use of camera & microphone

## Slide 38: 3.5 Given a scenario, implement secure mobile solutions
Mobile Device Management (MDM)
  Context-Aware Authentication
    Location-based and situational
    Combine multiple contexts
      Where you normally login (IP address
      Where you normally frequent (GPS information
      Anti-virus and security posture status
    Context-aware security, example:
      Allow authentication from within the United States anytime
      Allow authentication if the user is accessing email or a shared file system
      Do not allow authentication if the AV program is two days out of date
      Do not allow authentication if the location is outside of the country

## Slide 39: 3.5 Given a scenario, implement secure mobile solutions
Deployment models
  BYOD (bring your own device)
    Employees are able to bring personally owned devices into a corporate computing environment
    Does not necessarily prevent the transfer of corporate information to the device
    There is no standardization
    Employees do not replace their devices often enough to keep them running efficiently
    The company does not have enough control over the devices
    Require applications to be digitally signed to decrease the risk of users jailbreaking mobile devices
    Containerization of company data
  CYOD (choose your own device)
    Employee is permitted to choose from a selection of approved devices
    The company owns the device
    Standardized deployment
    Allows employees to make personal use of devices

## Slide 40: 3.5 Given a scenario, implement secure mobile solutions
Deployment models
  COBO (Corporate-Owned Business Only)
    Organization purchases devices and issues them to employees
    Devices are heavily restricted and only used for work
    Most secure, but rigidity impacts productivity
  COPE (corporate-owned, personally enabled)
    The company owns the device
    Standardized deployment
    Employee does not necessarily have the ability to choose the device
    Allows employees to make personal use of corporate-owned devices
    Limited choice of devices
    Much easier to support than BYOD

## Slide 41: Mobile / Wireless Attacks

## Slide 42: Rogue Access Points and Evil Twins
Rogue access point
  Troubleshooting access point misconfiguration
  Disable unused devices and interfaces
Evil twin
  Masquerade as legitimate AP
  Use similar SSID
  Capture authentication information

## Slide 43
A security administrator has been using EAP-FAST wireless authentication since the migration from WEP to WPA2. The company’s network team now needs to support additional authentication protocols inside of an encrypted tunnel. Which of the following would meet the network team’s requirements?
    EAP-TLS
    PEAP
    EAP-TTLS
    EAP-MSCHAPv2
A system administrator has configured MAC filtering on the corporate access point, but access logs show that unauthorized users are accessing the network. The administrator has confirmed that the address filter includes only authorized MAC addresses. Which of the following should the administrator configure to prevent this authorized use?
    Enable WPA3 encryption
    Remove unauthorized MAC addresses from the filter
    Modify the SSID name
    Modify the channel
A security administrator would like use employee-owned cell phones to unlock the door of the data center using a sensor on the wall. The users would authenticate on their phones with a fingerprint before the door would unlock. Which of the following features should the administrator use? (Select TWO)
    NFC
    Remote Wipe
    Containerization
    Biometrics
    Push notification
Answer the questions…
Notes: Answers:
C. EAP-TTLS (EAP-TTLS (Extensible Authentication Protocol - Tunneled Transport Layer Security) allows the use of multiple authentication protocols transported inside of an encrypted TLS (Transport Layer Security) tunnel. This allows the use of any authentication while maintaining confidentiality with TLS.
2. A. Enable WPA3 encryption
A MAC (Media Access Control) address can be spoofed on a remote device, which means anyone within the vicinity of the access point can view legitimate MAC addresses and spoof them to avoid the MAC filter. To ensure proper authentication, the system administrator can enable
WPA3 (Wi-Fi Protected Access version 3) with a shared key, or configure 802.1X to integrate with an existing authentication database.
The incorrect answers:
B. Remove unauthorized MAC addresses from the filter - Since MAC addresses are visible when capturing packets, any unauthorized users affected by the removal of a MAC address would simply obtain the remaining MAC addresses in use and spoof those addresses to gain access.
C. Modify the SSID name - The SSID (Service Set Identifier) is the name associated with the wireless network. The name of the access point is not a security feature, so changing the name would not provide any additional access control.
D. Modify the channel - The frequencies used by the access point are chosen to minimize interference with nearby wireless devices. These wireless channels are not security features and changing the frequency would not limit unauthorized access.
3. The Answer: A. NFC and D. Biometrics
The wall sensor will be activated with the phone’s NFC (Near-field Communication) electronics and would authenticate using the biometric
fingerprint reader on the phone.
The incorrect answers:
B. Remote wipe - Although remote wipe can be a useful management tool for a mobile device, there’s no need to include remote wipe capabilities with this particular application. The door unlocking process would still require authentication using the user’s fingerprint if the phone was lost or stolen.
C. Containerization - This application doesn’t appear to store any confidential local data, so keeping the enterprise data separate from the personal data isn’t a significant concern.
E. Push notification - A push notification will cause alerts to appear on the phone without any user intervention. In this app, all the actions are initiated by the user.

## Slide 44: Questions?

## Slide 45: 8. Securing Wireless & Mobile Solutions
3.4 Given a scenario, install and configure wireless security settings
3.5 Given a scenario, implement secure mobile solutions